## Slide 1: Intro to Sensors 101 with Raspberry Pi – Rotation 1
David Crook
@Data4Bots
Questions: dacrook@Microsoft.com

## Slide 2: Agenda
The ‘me’ slide
Things to know
Goals
Content
Summary
Continuous Q&A

## Slide 3: David Crook
Microsoft Developer Evangelist
Focused on Machine Learning and Embedded Systems
Enjoys challenges
Likes Fishing + Brazilian Jiu Jitsu
  Typically not together
dacrook@Microsoft.com
(980)228-6278
@Data4Bots
www.indiedevspot.com

## Slide 4: Stuff you should Know About
Additional Resources
  Channel9: http://channel9.msdn.com
  Hackster: https://www.hackster.io
  Stack Overflow: http://electronics.stackexchange.com/
BizSpark
  Free Azure
  Free Tools Network Partner Give to your startups for free
Microsoft Innovation Center
  Hack Tuesdays: Mentoring every Tuesday 11am – 4pm
  Free Co-Working for Startups: dacrook@Microsoft.com to apply
  Free Training: See schedule here: http://indiedevspot.com/events/

## Slide 5: Future Reference Getting Started
http://ms-iot.github.io/content/en-US/GetStarted.htm

## Slide 6: Get the Codes
https://github.com/drcrook1/MTPSolution

## Slide 7: Goals of Presentation
Understand Raspberry SPI Interface
Understand ADC and purpose
Collect Data from Light, Temperature and Pressure
Debug to verify values.

## Slide 8
Will not concern
ourselves with:
I2C
Focus just on
Power
Ground
Gpio
SPI
Physical Pin
vs
Logical Pin

## Slide 9: How a Breadboard works

## Slide 10: Understand ADC – MCP3008
Data Sheet: http://ww1.microchip.com/downloads/en/DeviceDoc/21295d.pdf
8 Channel, 10 Bit, Duplex Communication
  8 Analog Inputs
  10 bit value resolution (0-1023 value range)
  Send/Receive same operation and byte size.
Explain Pins
  Vdd/Vref – power and ref voltage
  Clk – data transfer speed
  CS – Channel Select
  Dout/Din – data lines
  Agnd/Dgnd - grounds

## Slide 11: Duplex Data with 8 bit (1 byte) Segments
Notes: We are concerned with 8 bit segments as most Microcontrollers (Pi included) communicate purely on 8bit segments, while the ADC is 10 bit.
10 bit resolution as in the MCP3008 means to initiate a data receive sequence you need to transfer 2 bytes, last bit of the first byte says next coming byte is the channel mode and channel. The next two bytes, the first bit is null, the next 10 are data and the rest are null.

## Slide 12: Code – Read ADC Value from Channel x
public int ReadValue(int channelNumber)
{
if ((channelNumber < 0) || (channelNumber > ChannelCount)) throw new ArgumentOutOfRangeException("channelNumber");
EnsureInitializedAsync().Wait();
byte[] writeBuffer = new byte[3] { 0x00, 0x00, 0x00 };
byte[] readBuffer = new byte[3];
UInt16 command = 0x0;
if (ChannelMode == ProviderAdcChannelMode.Differential)
{
int shiftLeftNum = 8; // 15 - 7
int channelShifter = 13;
command = (UInt16)((0x01 << shiftLeftNum) |((Int16)channelNumber << channelShifter));
}
else
{
int shiftLeftNum = 8; // 15 - 7
int channelShifter = 13;
command = (UInt16)((0x03 << shiftLeftNum) | ( (Int16)channelNumber << channelShifter ) );
}
var commandBytes = BitConverter.GetBytes(command);
writeBuffer[0] = commandBytes[1];
writeBuffer[1] = commandBytes[0];
spiDevice.TransferFullDuplex(writeBuffer, readBuffer);
int result = readBuffer[1] & 0x03;
result <<= 8;
result += readBuffer[2];
return (int)result;
}
Notes: Don’t worry, this is already written…
Write Buffer and Read Buffer are same due to communication in Duplex, every bit written is also outputted to both devices.
Leading bits is established based on resolution of ADC such that the beginning of the data bits lines up with actual bytes.
In this instance:
Sent Bits
0000 0001 – byte 1 – this one is the start listening command
1111 0000 – byte 2 - this is single mode (first bit) and 7th channel, 7 in bits is 111, for channel 0, 000 would follow the 1, for channel 1 – 001
Second half of byte is ignored
0000 0000 – byte 3 – ignored by adc
Received Bits
0000 0001 – byte 1 duplex, input is output
1111 00dd – byte 2 duplex, input is output, second half of byte is null bit + falling cycle (basically null)
dddd dddd– byte 3 bit is all data
Therefor, we mask getting only last two bytes of byte 2 and read as int, shift whole thing to more
significance and then add the last byte (which is auto-cast to an int by C#)

## Slide 13: Schematic

## Slide 14: Wiring Diagram
Make sure correct before powering on
Notes: Mosi – Master Out, Slave in matches to MCP3008 Data In
Miso – Master In, Slave out matches to MCP3008 Data Out
SCLK – Matches to MCP CLK
CS0 – Matches to MCP CS

## Slide 15: Connect Pis and Download Code
Ethernet Cable to Adapter to Computer USB
Power On Pi
Download the Zip
  https://github.com/drcrook1/MTPSolution
  Then extract it

## Slide 16: Open the Code
Open Visual Studio 2015 Community
  Excellent programming tool.
Double Click .sln file
  Opens in VS 2015

## Slide 17: Set Build for your Device
Right Click Project
  Properties (at the bottom)
ARM
Remote
Your IP
No Auth

## Slide 18: Deploy && Debug
Set to ARM
Click In Gray Area
  Creates red breakpoint
Click Green Arrow
You can remove breakpoint and click green arrow to continue.

## Slide 19: How it Works
Nuget Package
Extended through MTP.IoT Project
  Project reference, added new ADC controller for MCP3008 which is in the kit
Use peripherals and management system provided by IoT.Devices

## Slide 20: Code Walk Through
Notice extensive comments 

## Slide 21: On your own

## Slide 22: Add a Temperature Sensor
TMP36GZ http://www.analog.com/media/en/technical-documentation/data-sheets/TMP35_36_37.pdf
  Double check correct power/ground
    It will possibly catch fire if backwords.
    Will definitely melt
Pin 1 = Power (+5V)
Pin 2 = Reading (analog out)
Pin 3 = Ground

## Slide 23: Conversion
For every degree C, produces 10 mV
ADC produces measurements in: V
1 V = 100 mV – Therefor: Reading / 10 = Deg C
Convert to F = ( (9/5) * Cel ) + 32

## Slide 24: What Next?

## Slide 25: Baby Thermostat!
Is it too hot for baby?
  Turn on the Fan!
Too cold for baby?
  Turn off the Fan!

## Slide 26: Light and Temp Tracking Camera
Use 2 of each sensor
Find a signature and follow it!

## Slide 27: There is more!

## Slide 28: Brown Bag Series
Electronics 101
  3 Rotating Sessions
IoT 101
  3 Rotating Sessions
Machine Learning 101
  2 Rotating Sessions
3D Printing 101
  Just 1 session!

## Slide 29: Questions?

## Slide 30
dacrook@Microsoft.com
(980)228-6278
@Data4Bots
www.indiedevspot.com