## Slide 1: Initial Setup Raspberry Pi
David Crook
@Data4Bots
Questions: dacrook@Microsoft.com

## Slide 2: Agenda
The ‘me’ slide
Things to know
Goals
Content
Summary
Continuous Q&A

## Slide 3: David Crook
Microsoft Developer Evangelist
Focused on Machine Learning and Embedded Systems
Enjoys challenges
Likes Fishing + Brazilian Jiu Jitsu
  Typically not together
dacrook@Microsoft.com
(980)228-6278
@Data4Bots
www.indiedevspot.com

## Slide 4: Stuff you should Know About
Additional Resources
  Channel9: http://channel9.msdn.com
  Hackster: https://www.hackster.io
  Stack Overflow: http://electronics.stackexchange.com/
BizSpark
  Free Azure
  Free Tools Network Partner Give to your startups for free
Microsoft Innovation Center
  Hack Tuesdays: Mentoring every Tuesday 11am – 4pm
  Free Co-Working for Startups: dacrook@Microsoft.com to apply
  Free Training: See schedule here: http://indiedevspot.com/events/

## Slide 5: Future Reference Getting Started
http://ms-iot.github.io/content/en-US/GetStarted.htm

## Slide 6: Goals of Presentation
Understanding the Pi
Installing Windows 10 IoT Core
Power Considerations
Wi-Fi Options
PowerShell Setup

## Slide 7: What is the Raspberry Pi?
Compared to Arduino

## Slide 8: What is Windows 10 IoT Core
Why not Raspbian

## Slide 9: Why do I care about them?
Power
IoT
Development Tools
  Languages
  Libraries
  Visual Studio
Dev Ops Tool Chain
  Visual Studio
  Build

## Slide 10: Wi-Fi Options
Official Raspberry Pi Dongle
  Simple setup
  Possible issues if multiple on same network (all are default named minwinpc)
Ethernet Adapter (included in PG Kits)
  More difficult setup
  More robust setup

## Slide 11: PowerShell Setup
Headless
  No UI, No Keyboard
Ethernet Adapter
  Comes with PG Kit
  Official dongles are nearly impossible to get.
Remember Power Considerations
  USB power packs might supply 5V, but not enough Amps

## Slide 12: Connect Everything
Supply Pi with Power
Connect Ethernet Cable to Adapter to USB into laptop

## Slide 13: Enabling Wi-Fi Bridging
Open Control Panel
Navigate to Network and Internet
Navigate to Network & Sharing
Click Ethernet
Go to Properties
Select IPV4
Select Properties

## Slide 14: Enabling Wi-Fi Bridging Cont.
Set your Ip Address to 192.168.1.1
Set your Subnet mask to 255.255.255.0
Close and Save settings
Download: http://www.dhcpserver.de/
Extract and run wizard

## Slide 15: Enabling Wi-Fi Bridging Cont. Cont.
Select Ethernet (notice DHCP is disabled)
Do not select other protocols
Accept default configurations
Click “write ini file”
Click Finish
Click “Continue as tray app”
Click allow access on firewall setup

## Slide 16: Enabling Wi-Fi Bridging Cont. Cont. Cont.
Boot up the pi.
Notice a popup for a new ip address.

## Slide 17
Will not concern
ourselves with:
I2C
SPI
Focus just on
Power
Ground
Gpio
Physical Pin
vs
Logical Pin

## Slide 18: How a Breadboard works

## Slide 19: Circuit Schematics – Symbols – LED Sample
Resistor
Ground
Power
LED

## Slide 20: Wiring Diagram

## Slide 21: Blinking the light
Open Visual Studio 2015 Community
  Excellent programming tool.
Create new Project and Solution
  File -> New -> Project

## Slide 23: Getting Set Up
Add a Reference
  Right Click -> Add Reference
Windows IoT Extensions for the UWP
  Under Universal Windows
  In Extensions
  Select
  Click Ok

## Slide 24: Have these using statements
using System;
using Windows.ApplicationModel;
using Windows.ApplicationModel.Activation;
using Windows.Devices.Gpio;
using Windows.UI.Xaml;
using Windows.UI.Xaml.Controls;
using Windows.UI.Xaml.Navigation;
Have these class level private variables
In the file App.Xaml.cs
private const int ledPinNumber = 27;
private GpioPin ledPin;
private GpioPinValue ledVal;
private DispatcherTimer timer;

## Slide 25: Modify the Constructor
public App()
{
Microsoft.ApplicationInsights.WindowsAppInitializer.InitializeAsync(
Microsoft.ApplicationInsights.WindowsCollectors.Metadata |
Microsoft.ApplicationInsights.WindowsCollectors.Session);
this.InitializeComponent();
this.Suspending += OnSuspending;
//Add these lines
InitGPIO();
InitBlinky();
}

## Slide 26: Initialize GPIO
private void InitGPIO()
{
var gpio = GpioController.GetDefault();
if (gpio == null)
{
throw new Exception("Gpio expected on this device");
}
ledPin = gpio.OpenPin(ledPinNumber);
ledPin.SetDriveMode(GpioPinDriveMode.Output);
ledPin.Write(GpioPinValue.Low);
ledVal = GpioPinValue.Low;
}

## Slide 27: Initialize Blinking
private void InitBlinky()
{
timer = new DispatcherTimer();
timer.Interval = TimeSpan.FromMilliseconds(500);
timer.Tick += Timer_Tick;
timer.Start();
}

## Slide 28: Add Handler for Timer Tick
private void Timer_Tick(object sender, object e)
{
if(ledVal == GpioPinValue.High)
{
ledPin.Write(GpioPinValue.Low);
ledVal = GpioPinValue.Low;
}
else
{
ledPin.Write(GpioPinValue.High);
ledVal = GpioPinValue.High;
}
}

## Slide 29: Set Build for your Device
Right Click Project
  Properties (at the bottom)
ARM
Remote
Your IP
No Auth

## Slide 30: Deploy && Debug
Set to ARM
Click In Gray Area
  Creates red breakpoint
Click Green Arrow
You can remove breakpoint and click green arrow to continue.

## Slide 31: Take a breather

## Slide 32: Circuit Schematics – Symbols – MOTORS!
Transistor
Diode
Motor

## Slide 33: The Data Sheet – Part 1
We have: PN2222A

## Slide 34: The Data Sheet – Part 2
Important here is
  Maximum ratings

## Slide 35: The Data Sheet – Part 3

## Slide 36: Wiring Diagram

## Slide 37: The Code…
Remains EXACTLY the same 
We are switching the motor on/off every 500 milliseconds, just like we did with the LED.

## Slide 38: What Next?

## Slide 39: Create a car!
Control 4 motors
Create functions for:
  Left
  Right
  Forward
  Back

## Slide 40: Control a Sprinkler System!

## Slide 41: There is more!

## Slide 42: Brown Bag Series
Electronics 101
  3 Rotating Sessions
IoT 101
  3 Rotating Sessions
Machine Learning 101
  2 Rotating Sessions
3D Printing 101
  Just 1 session!

## Slide 43: Questions?

## Slide 44
dacrook@Microsoft.com
(980)228-6278
@Data4Bots
www.indiedevspot.com